## Slide 1: Small Adaptable Mother Ship Design Space Exploration
PF Naughton
29 February 2020

## Slide 2: Project Summary
This presentation summarizes an early stage design space exploration for small, ocean-going, vessels optimized to serve as mother ships for automated and/or autonomous (A&A) small craft, including;
  Investigation of Potential Roles for a Small Adaptable Mother Ship (SAMS)
  Parametric Analyses of Dimensions and Weights
  Investigation of Design Constraints
  Analyses of Unique Design Features, particularly in way of Powering and Organic Overboard Vehicle (OOV) handling features
  Investigation of any special design evaluation tools
Analyses of design space key to successful SBD process

## Slide 3: Target Market
MCMVs and AGORs frequently employ remotely piloted vehicles (and more recently A&A small craft)
Many NATO and friendly navies in need of replacing legacy Mine Counter Measures Vessels (MCMVs)
Also ongoing need for oceanographic vessels (AGORS), Offshore Patrol Vessels (OPVs) and other ancillary naval vessels
Dedicated, single-role vessels can be expensive due to
  short production runs
  stringent design requirements (such as low signatures)
  need to accommodate mission specific equipment
SAMS outfitted with modular A&A systems can provide navies with a relatively low cost, multi-use platform, to take the place of multiple one-off or limited run specialized vessels

## Slide 4: Innovations
Legacy MCMVs typically specially designed low-signature/shock resistant/high-cost vessels, with limited range and endurance
Use of A&A craft can now allow MCMVs to;
  stand off from immediate threat area,
  deploy unmanned craft to detect and neutralize mine threats,
Allows for a simpler, less costly mothership to perform the same role
  Also potential to increase propulsion power and vessel range for Mother Ship due to use of simpler (less noise controlled and shock resilient) propulsion plant
One Mother Ship can be re-outfitted to perform different roles throughout its service life (including research, law enforcement, and low intensity naval roles) reducing need to maintain multiple specialized vessel types

## Slide 5: Competition
US currently committed to LCS for future MCM mission
  However still ongoing need for future research vessels
Belgian and Dutch Navies recently signed a contract for twelve 81m MCMVs designed to employ A&A type overboard craft
  DAMEN had also submitted a 91m “Mother Ship” for this contract
SAAB is currently marketing an 80m MCMV platform & BMT is marketing an 85m platform
  both designed to support the use of A&A craft in the MCM mission
RN has previously investigated a single platform for future Hydrographic Research and Mine Counter Measures needs
Existing Design Tools such as ASSET and RSDE mostly aimed at larger (FF, DD, and CG) sized surface combatants

## Slide 6: Parametric Analyses of Dimensions & Weights
Collected weight and dimensional data for a wide range of legacy modern naval vessels and design studies into a single EXCEL Spreadsheet
Reviewed data for design trends
Sample Database Plots
Database consists weights and dimensional data for,
3-Digit SWBS 100-700 (13 vessels)
3-Digit SWBS 100 only (16 vessels)
1-Digit SWBS 100-700 (additional 37 vessels)
Dimensional data on 271 additional small combatants

## Slide 7: Potential Length Constraints
  Design Length
  > 91m (300ft) - damage length of 15%L for combatants
  12.5%L for auxiliaries (often includes OPVs)
  < 91m (300ft) - 2-compartment flooding
  Maximum fire zone length - 40m (131ft)
    Vessels < 75-80m (245-260ft) often require only two main fire zones (reducing the need for additional fire pumps, piping, fitting & insulation)
Required stack up length can be a limiting factor for designs
Sample Arrangements & Hullform Tool

## Slide 8: Current Status & Recommendations
A design space exploration for small, ocean-going, vessels optimized to serve as mother ships for automated and/or autonomous (A&A) small craft was initiated
  A database of small vessels was compiled
  Weight and dimensional trends have been reviewed
  Potential design constraints have also been identified
  Simple tools to help evaluate specific constraints have been looked into
This analyses can assist in early stage concept design and estimating for small vessels suitable for use as a SAMS
Further work on:
  Expanding the database
  Exploring length constraints (including floodable lengths), machinery options (including space and weight imapcts), and OOV handing concepts can be beneficial to assist in assessing feasibility of future mothership concept designs

## Slide 9: Power Plant Considerations
  Power Plant Configuration
  Because SAMS may end up spending large amount of time at low speeds (<6-8kts) deploying/retrieving and/or operating craft, need either;
    main propulsion plant that can operate reliably and efficiently at low speeds, or
    auxiliary propulsor specifically for lower speeds operations
Loiter operations likely to play a major role in selection of propulsion machinery

## Slide 10: OOV Handling Features
Modern OOV Handling Methods
Historical Concepts to attenuate relative motions
Relative Motions & Velocities between Mothership and OOVs play a big role in ability to launch/recover OOVs
  Means of reducing differences in relative motions can improve launch/recovery capabilities

## Slide 11: OOV Stowage Features
Modern Hangar/Mission Zone Concepts
  Potential exists to increase flexibility of onboard stowage spaces
Potential Future Concepts